## Slide 1
LIM
Yoram Yaniv, October 2010

## Slide 2: VENµS Vs. Galex (1)
VENµS | Galex | 
IMPS by IAI/MBT Space (Based on TecSar satellite design) | LEOStar-2 by Orbital (based on Orbview4 satellite design) | Original Bus
4.5 years | 2.5 years | Mission Duration
720km, Sun Syn. | 690km, inclination 29º | Orbit
245kg (inc. Tech payload ~25kg) | 280kg | Dry mass
25cm, f/7 (l=1.75m) | 50cm, f/6 | Telescope size

## Slide 3: VENµS Vs. Galex (2)
VENµS | Galex | 
310Mbits/sec | 25 Mbits/sec | X Band
15 Kbits/sec | 2 Mbits/sec | S Band
Solar Panels 850 watts, Battery 30 Ah | Solar Panels 3 m², Battery | 
3 axis stabilized, 2 Gyros, 4 reaction wheels, magnetic torques bars, sun sensors, Star Trackers | 3 axis stabilized, 2 Gyros, 4 reaction wheels, magnetic torques bars, sun sensors, Star Trackers | Attitude Control
240 Gbits | ? | On Board Recorder

## Slide 4: LIM – Cost Reduction (1)
Dual launch
Low operation
Use existing design and units – adapt the mission requirements to existing design and units
Additional missions to exploit bus capabilities – cost reduction per specific mission

## Slide 5: LIM – Cost Reduction (2)
On board computer based on includes ~10Gbit (no On Board Recorder)
Communication
  Existing systems: Single ground station (S + X)
  TDRSS
  BGAN (including GPS?)
No propulsion system
No Star Trackers (Magnetometers, Sun sensors, Gyro)

## Slide 6: LIM System

## Slide 7: Orbit
06:00 orbit (sun is perpendicular to the orbit plane)
  No eclipse, constant power supply, small battery
  Size of solar panel depend on imaging cover (recommended no more than hemisphere)
  Imaging to the opposite direction of the sun
  Routine thermal behavior
  Scanning around cone (gyro) or “Jump” from one image to the next image
  Poor pointing accuracy for “pre” (0.5º), good pointing accuracy (~0.01º?) for “post” (on the ground from image)

## Slide 8: IR Detector